## Slide 1: Scratch VHDL Hands-on FPGA Experience Education Tool
Philip & Joseph Abbey
https://house-of-abbey.github.io/scratch_vhdl/

## Slide 2: Field Programmable Gate Array (FPGA)
A “sea of gates” waiting to be connected up
  Each gate needs to be given a function
    Typically a 6-input lookup table (LUT)
    Register (D-Flop)
  Each gate needs to be connected
    Paths between gates need to be defined for inputs and outputs
    Clock and reset nets connected
    See “Interconnection Resources”
Runtime definitions held in SRAM
  Dumb at power on
    Until programmed with a BIT file
  Forgotten at power off
    Needs to be re-programmed next time
E.g. Xilinx UltraScale+ FPGA:
  8,938 k system logic cells
  3,840 multipliers, each 27 bits x 18 bits
  224 Mb memory
  2577 I/O pins
https://www.eetimes.com/all-about-fpgas/
They're Big!

## Slide 3: FPGA Applications
Video imaging
Military technologies, including
  Cryptography
  Missile guidance systems
Automotive computing
Aerospace applications
Search engine algorithms
Networking and data center management
Digital Signal Processing (DSP)
Medical devices
Ability to perform many data operations simultaneously
  A general-purpose processor normally does one task and moves on to the next
  Custom computation to exploit parallelism in algorithms
Special-purpose hardware without the costs associated with fixed logic silicon chips (ASICs ⴕ)
  But not as ‘fast’
  i.e. lower clock speed
Middle ground between software and ASIC
ⴕApplication Specific Integrated Circuit (ASIC)

## Slide 4: Scratch VHDL Full Design
PLL
Synchroniser (retime)
Synchroniser (retime)
External clock
4
4
sw(3:0)
btn(3:0)
Power-on Reset
zybo_z7_10
led(3:0)
reset
clk
led4_button4
buttons(3:0)
leds(3:0)
7 Segment Display Decoder
clk
leds(3:0)
sevseg(6:0)
Reprogramme this component

## Slide 5: led4_button4 Specification
The only part of the design you need to work is this component
  clk, reset and incr, are given to you
    Use incr as a condition in order to slow down a sequence of actions for the naked eye
  4 button in buttons(3:0)
  4 LEDs in leds(3:0)
led4_button4
clk
reset
incr
buttons(3:0)
leds(3:0)

## Slide 6: Essential Knowledge
D
Q
CE
Purely combinatorial logic
Registered logic
Process sensitivity list
Clock specification
Reset state
Actions
{
{
{
Combinatorial logic
{
Combinatorial logic

## Slide 7: Code Your 1st Scratch VHDL Example
E.g. Logic gates
Code & Compile
Simulate & Test
Synthesise
Programme & Test

## Slide 8: Design Process
Design Entry
Scratch to generate VHDL
Simulation
Stimulate the design to test functionality
Synthesis
Place & Route (Implementation)
Elaboration
Synthesis
Programming
BIT file generation
Program and Test
Choose a project
Button GUI rather than VHDL test bench
Experience the end-to-end design entry and build process without having to learn VHDL


## Slide 9: Simulation Setup
The main test stimulus is provided by a clickable GUI
  4 buttons
  3 LEDs
The GUI interacts with a VHDL test bench
  But you don’t need to see it.
The simulation wave window then needs to be used to debug the design
reset
clk
led4_button4
buttons(3:0)
leds(3:0)
reset
clk
Stimulus
test_zybo_z7_10

## Slide 10: Simulation Controls
Start Emulation
Set Assembly File for ROM
Make the display reflect the state under the cursor
Three tabs for different displays and button types
Step Emulation
Restart the simulation and reset the GUI
Four buttons

## Slide 11: Design Process
Design Entry
Scratch to generate VHDL
Simulation
Stimulate the design to test functionality
Synthesis
Place & Route (Implementation)
Elaboration
Synthesis
Programming
BIT file generation
Program and Test
Choose a project
Button GUI rather than VHDL test bench
Experience the end-to-end design entry and build process without having to learn VHDL



## Slide 12: Create the FPGA Programming File
Elaborate
Verify gates
Synthesise
Verify LUT truth tables
Implement
Check timing
Check timing
Program FPGA
Test design
Verify gate placement
Use the Vivado ‘synthesis’ tool as instructed:

## Slide 13: What does “Check Timing” mean?
TSU
Data
Clock
Logic
Slack
Clock Period (s) = TP
D
Q
D
Q
TH
Setup time before clock edge = TSU
Hold time after clock edge = TH
Maximum clock frequency:
(Hz)
‘Slack’ = ‘spare time’
for a desired target clock speed ≤
The exercises are constructed so that this real-world issue does not become a problem.

## Slide 14: Exercise 2
Repeat the previous steps for a more involved example.
  Pick an example with ‘state’ from:
    Pulse Generator, shortening a long pulse to a short one.
    Shift Register, use a button to choose the status of LED 0, all the LEDs continue to scroll to the left.
      This can be developed into sequences that go back and forth for a bi-directional shift register controlled by two buttons, each inserting a lit LED into one end and changing the direction of shift.
    4-bit binary counter with start and stop buttons.
    Sum of buttons pressed.
      This come in two variations, one-hot and binary.
      The former lights a single LED based on the number of buttons pressed at any one time.
      The latter represent the number of buttons in binary 0-4.
    The Knight Rider
      KITT car bonnet light sequence from the 1980’s television series.
    Traffic lights
      Comes in two variations; the standard junction and the Pelican crossing.
      The latter (of course ;-) includes a flashing yellow stage.
    Dimmer Controller
      Two buttons increase or decrease a control value, e.g. the brightness of a room light
      The LEDs signifying the size of the value being controlled.
    Linear Feedback Shift Register
      GF(2n) mathematics!
      Pseudo random sequences

## Slide 15: Final Example
Take the parts given to you to simulate and synthesise an embedded ‘software’ design.
  Compile the 4-bit RISC CPU
  Choose a software instruction file
  Simulate & synthesise the design
  Test it on hardware
Modify the software instruction file
  Edit the instructions
  Assemble the code
  Re-simulate, re-synthesise, re-test on hardware

## Slide 16: 4-bit RISC CPU
The 4-bit CPU is specialised to 4 buttons and 4 LEDs
The instructions are compiled into the FPGA design
  Uses a ROM not RAM
  CPU ‘registers’ will hold your state
Develop software to light LEDs and react to the buttons
reset
clk
led4_button4
buttons(3:0)
leds(3:0)
ROM
RISC CPU
reg(7)
reg(6)
customasm
file. asm
file.o

## Slide 17: Our ALU Design
In the given design:
  Only 16 instructions
  6 working registers
  2 special registers for
    Reading the button state
    Writing the LED state
Executes ‘operations’
  On 2 input registers
  Writing back to an output register
  E.g. r5 = r3 AND r4
r0
r1
r2
r3
r4
r5
btns
leds
ALU
5:3
2:0
8:6
o
a
b
12:9
op
o <- a op b
Assembled instructions are 13-bits long
6 registers, but no RAM. 2 “special” registers

## Slide 18: Assembly of Instructions
Easiest to code by reviewing examples given
Then refer to the reference when you have familiarity
  https://house-of-abbey.github.io/scratch_vhdl/risc_cpu.html#candidate-instructions
#include "./ruledef.asm"
r0 <- 3
r1 <- 0b0000
loop:
leds <- r0 + btns
wincr 3
leds <- btns and r1
wincr 1
goto loop
0001000000011
0001001000000
0110111000110
1110000000011
0011111110001
1110000000001
1111000000010
add.asm
add.o
Assembly
customasm.exe