## Slide 1: Scratch VHDL Hands-on FPGA Experience Education Tool
Philip & Joseph Abbey
https://house-of-abbey.github.io/scratch_vhdl/

## Slide 2: Design Process
Design Entry
Scratch to generate VHDL
Simulation
Stimulate the design to test functionality
Synthesis
Place & Route (Implementation)
Elaboration
Synthesis
Programming
BIT file generation
Program and Test
Choose a project
Button GUI rather than VHDL test bench
Experience the end-to-end design entry and build process without having to learn VHDL

## Slide 3: Design Entry – Scratch in VSCode
library ieee;
use ieee.std_logic_1164.all;
architecture scratch of led4_button4 is
constant button_tab_c : natural := 1;
signal run : std_logic;
signal state : integer range 0 to 5 := 0;
alias start is buttons(0);
alias stop is buttons(1);
begin
process(clk)
begin
if rising_edge(clk) then
if reset = '1' then
run <= '0';
state <= 0;
leds <= "0000";
else
if start = '1' then
run <= '1';
elsif stop = '1' then
run <= '0';
end if;
if run = '1' and incr = '1' then
if state = 5 then
state <= 0;
else
state <= state + 1;
end if;
case state is
when 0 =>
leds <= "0001";
when 1 =>
leds <= "0010";
:
Generates VHDL

## Slide 4: VHDL Simulation - ModelSim

## Slide 5: Elaboration to Generic Gates - Vivado
Simplified to “buttonology”

## Slide 6: Synthesis to Xilinx Device - Vivado

## Slide 7: Execution – Zybo Z7
Toggle Buttons
Push Buttons
LEDs

## Slide 8: Concept
Simple range of designs
  Bite-sized to make you think a little
Testing reduced to ‘interactive play’
  Skip the self-checking test benches for this exercise
Full Design Process Introduction
  Simulation
  Synthesis
  Development Board
Superficial but hands-on

## Slide 9: Example Projects
Foundation
One LED per button
  Hello World
Logic gates
  Truth tables
Pulse Generator
Shift Register
4-bit binary counter
Sum of buttons pressed
State Machines
The Knight Rider KITT car
  Bonnet light sequence from the 1980’s television series
Traffic lights
  Standard junction
  Pelican crossing
Dimmer Controller
Linear Feedback Shift Register
RISC CPU

## Slide 10: Finally - 4-Bit RISC CPU
Custom CPU instruction set
  Designed for “4 buttons and 4 LEDs”
Custom assembler
  Modified from existing Open Source project
#include "./ruledef.asm"
pelicon_crossing:
.s0:
leds <- 0b0001
wincr
r0 <- 0b0001 ; start
.s0_loop:
r1 <- btns and r0
if r1 eq r0
goto .s1
goto .s0_loop
.s1:
leds <- 0b0011
wincr
.s2:
leds <- 0b0000
wincr
.s3:
leds <- 0b0010
wincr
.s4:
leds <- 0b0000 ; Left filter this time
wincr
.s5:
leds <- 0b0010
wincr
.s6:
leds <- 0b0100
wincr
r0 <- 0b0010 ; stop
.s6_loop:
r1 <- btns and r0
if r1 eq r0
goto .s7
goto .s6_loop
.s7:
leds <- 0b0010
wincr
goto pelicon_crossing

## Slide 11: Instruction Set
Forked from https://github.com/hlorenzi/customasm
See https://github.com/JosephAbbey/customasm
Assemble code for your own instruction set
#once
#bits 13
; Define a register
#subruledef reg
{
btns => 6`3 ; equivalent to r6
leds => 7`3 ; equivalent to r7
r{r:u3} => r`3
}
; Safely assign the output register, make sure it is not r6, which is
; read-only for the buttons inputs.
#subruledef sreg
{
{o:reg} => {
assert(o != 6)
o`3
}
}
#subruledef condition ; VHDL references
{ ; op @ dest @ src1 @ src2
{a:reg}[{b:u2}] => 0xa @ 0`3 @ a`3 @ 0`1 @ b`2 ; op_ifbit
{a:reg} eq {b:reg} => 0xb @ 0`3 @ a`3 @ b`3 ; op_ifeq
{a:reg} gt {b:reg} => 0xc @ 0`3 @ a`3 @ b`3 ; op_ifgt
{a:reg} ge {b:reg} => 0xd @ 0`3 @ a`3 @ b`3 ; op_ifge
}
; In general: o = fn(a, b)
;
#ruledef ; VHDL references
{ ; op @ dest @ src1 @ src2
noop => 0x0 @ 0`9 ; noop
{o:sreg} <- {v:u4} => 0x1 @ o`3 @ 0`2 @ v`4 ; op_set
{o:sreg} <- {a:reg} => 0x2 @ o`3 @ a`3 @ 0`3 ; op_copy
{o:sreg} <- {a:reg} and {b:reg} => 0x3 @ o`3 @ a`3 @ b`3 ; op_and
{o:sreg} <- {a:reg} or {b:reg} => 0x4 @ o`3 @ a`3 @ b`3 ; op_or
{o:sreg} <- not {a:reg} => 0x5 @ o`3 @ a`3 @ 0`3 ; op_not
{o:sreg} <- {a:reg} + {b:reg} => 0x6 @ o`3 @ a`3 @ b`3 ; op_add
{o:sreg} <- {a:reg} - {b:reg} => 0x7 @ o`3 @ a`3 @ b`3 ; op_sub
{o:sreg} <- {b:u1} > {a:reg} => 0x8 @ o`3 @ a`3 @ 0`2 @ b`1 ; op_shft
{o:sreg} <- {a:reg} < {b:u1} => 0x8 @ o`3 @ a`3 @ 1`2 @ b`1 ; op_shft
if {c:condition} => c`13
wait until {c:condition} => asm {
if {c}
noop
goto $ - 2
}
wait while {c:condition} => asm {
if {c}
goto $ - 1
noop
}
wincr => 0xe @ 1`9 ; op_wi
wincr {l:u9} => 0xe @ l`9 ; op_wi
goto {l:u9} => 0xf @ l`9 ; op_goto
}

## Slide 12: 4-Bit RISC CPU Synthesis & Implementation

## Slide 13: Any Interest?
Need to prove this project works as an educational tool.

## Slide 14: Design Entry - Scratch
library ieee;
use ieee.std_logic_1164.all;
architecture scratch of led4_button4 is
constant button_tab_c : natural := 2;
begin
process(clk)
begin
if rising_edge(clk) then
if reset = '1' then
leds <= "0000";
else
case buttons is
when "0000" =>
leds <= "0000";
when "0001" | "0010" | "0100" | "1000" =>
leds <= "0001";
when "0011" | "0101" | "0110" | "1010" | "1100" | "1001" =>
leds <= "0010";
when "0111" | "1011" | "1101" | "1110" =>
leds <= "0011";
when "1111" =>
leds <= "0100";
-- Cover the other bit values: 'U', 'X', 'Z', 'W', 'L' & 'H'
when others =>
leds <= "1111";
end case;
end if;
end if;
end process;
end architecture;
Generates VHDL